## Slide 1: TOTAL PRODUCTIVE MAINTENANCE & TqM Looking after your equipment

## Slide 2: Learning Objectives
Understand the concept and philosophy of TPM
Learn the 8 pillars of TPM activities and step-by-step implementation approach
Learn the TPM tools and be able to identify and eliminate loss
Learn how to kick-start TPM deployment with Autonomous Maintenance, Planned Maintenance, Focused Improvement, and Education & Training activities to improve equipment effectiveness
Understand the roles of a TPM implementation organization and the critical success factors
Understand the TQM concept and philosophy

## Slide 3
“Maintenance is like looking after children. On a day-to-day basis you don’t require a doctor. In a factory your machines don’t require a technician. Production operators should think of their machines in the same way as a mother thinks of her children.”
Director of Maintenance Nissan UK

## Slide 4: Machine failures have many hidden causes
Failure
Loosening
Contamination
Corrosion
Leaks
Flaws
Deformation
Vibration
Cracks
Backlash
Improper
Temperature
Wear
Less
Visible
Visible
Failure is what we see but is only the tip of the iceberg
Minor machine defects are generally unnoticed but are the cause of almost all machine failures

## Slide 5: What is TPM?
Total Productive Maintenance (TPM) is a method to achieve maximum equipment effectiveness through employee involvement
Management + Operators + Maintenance

## Slide 6: What TPM is not?
A maintenance department program
Just a workshop or kaizen event
A way to eliminate skilled trades (maintenance staff, technicians, etc.)
Making operators and office staff into skilled tradesman

## Slide 7: Introduction to OEE
OEE (Overall Equipment Effectiveness) is a metric that identifies the percentage of planned production time that is truly productive
How to understand OEE score?
  An OEE score of 100% is perfect production
  An OEE score of 85% is world class for discrete manufacturers
  An OEE score of 60% is fairly typical for discrete manufacturers
  An OEE score of 40% is not uncommon for manufacturers without TPM and/or lean programs
What is your organization’s OEE score?

## Slide 8: World Class OEE
“World class” OEE is a standard which is used for comparison or benchmarking
For discrete manufacturing industry:
It should be cautioned that the “world class” OEE standard may not be applicable to all types of industries

## Slide 9: 3 Key Components of OEE
Component | TPM Goal | Type of Productivity Loss
Availability | No Breakdowns | Availability takes into account Downtime Loss, which includes all events that stop planned production for an appreciable length of time (typically several minutes or longer)
Performance | No Small Stops or Slow Running | Performance takes into account Speed Loss, which includes all factors that cause production to operate at less than the maximum possible speed when running
Quality | No Defects | Quality takes into account Quality Loss, which factors out manufactured pieces that do not meet quality standards, including pieces that require rework
OEE | Perfect Production | OEE takes into account all losses (Downtime Loss, Speed Loss, and Quality Loss), resulting in a measure of truly productive manufacturing time

## Slide 10: Six Big Equipment Losses
Overall Equipment Effectiveness
Availability
Breakdowns
Setups &
Adjustments
Performance
Reduced Speed
Minor Stops &
Idling
Quality
Startup &
Yield Loss
Defects &
Rework
Six Big Losses
Conveyors
Transport
Automatic welders
Presses
Paint processes
Molding machines
Machine tools
Presses
Transfer devices
Sensors
Automated assembly
Grinding
Presses
Seam welding
Raw material
Components
Fuel
Frequent Sites

## Slide 11: Visualizing OEE & the Six Big Losses

## Slide 12: Equipment Losses & OEE
Six Big Losses
Downtime
Losses
Quality
Losses
Speed
Losses
Fully Productive Time
Net Operating Time
Planned Production Time
Operating Time
Equipment
Average total operating loss
30-50%
Breakdowns
Setups & Adjustments
Reduced Speed
Minor Stops & Idling
Defects & Rework
Startup & Yield Loss
Breakdowns per machine (stopped longer than 10 mins) – less than once a month
Setup/adjustment time – less than 10 mins
Achieve ideal cycle times (design speed); increase 15% or more
Minor stoppages and idling per machine – under 10 mins
Rate (including products to be reworked) – less than 0.1%
Startup yield – 99% or more of lot
Ideal Cycle Time x Total Pcs
Operating Time
Good Pieces
Total Pieces
Operating Time
Planned Production Time
Availability
Quality
Performance
Greater than 90%
Throughput process
- Greater than 99%
Greater than 95%
OEE Factors
OEE = Availability x Performance x Quality
Source: Adapted from ‘TPM for Supervisors’, Productivity Press Development Team

## Slide 13: Improvement Goals for the 6 Big Losses
Type of Loss | Goal | Explanation
1. Breakdowns | 0 | Should be zero for all equipment
2. Setups and adjustments | minimize | As short as possible; less than 10 mins with zero adjustments
3. Reduced speed | 0 | Should match or – with improvements – exceed equipment specifications
4. Minor stoppages | 0 | Should be zero for all equipment
5. Defects and rework | 0 | Extent may vary, but goal should be expressed in parts per million (ppm)
6. Startup loss | minimize | 

## Slide 14: Breakdown losses
Largest of the 6 major equipment losses
Caused by equipment defects which require any kind of repair. Examples:
  Tooling failures
  Unplanned maintenance
  General breakdowns
  Equipment failure
Losses consist of downtime with labor and spare parts required to fix the equipment
Magnitude is measured by downtime.

## Slide 15: Set up and adjustment losses
Caused by changes in operating conditions, e.g. beginning of production runs or start-up at each shift, changes in products and conditions of operation
These losses consist of setup (equipment changeovers, exchanges of dies, jig and tools), start-up, and adjustment
Magnitude is measured in downtime

## Slide 16: Minor Stoppage Losses
Caused by events such as machine halting, jamming, idling, misfeeds, blocked sensors, etc.
Generally, these losses cannot be recorded automatically without suitable instruments
Formula: Losses = 100% - Performance Rate
Many companies regard such minor stoppages as breakdowns in order to emphasize their importance, even though no damage has occurred to the equipment

## Slide 17: Speed Losses
Caused by reduced operating speed – equipment cannot be operated at original or theoretical speed
At higher operating speeds, quality defects and minor stoppages frequently occur, resulting in operation at a lower moderate speed
Measure in terms of the ratio of actual operating speed to theoretical speed

## Slide 18: Quality Defect and Rework Losses
Caused by off-specification or defective products
  Rework
  Scrap
Losses consist of labor required to rework the products and the cost of the material to be scrapped
Measured by the ratio of quality products to total production
Sometimes designated as “quality defects in process” in order to distinguish from defective products during start-up and adjustment operations

## Slide 19: Start-up (Yield) Losses
Caused by unused or wasted raw materials
Exemplified by quantity of rejects, scraps, chips, etc.
Yield losses are divided into two groups
  Raw material losses resulting from product designs, manufacturing methods and equipment restrictions
  Adjustment losses resulting from quality defects associated with commencement of work, changeover, etc. Includes setup and adjustment losses plus yield losses, in terms of both time and material losses

## Slide 20: Sample OEE Calculation Using Excel
Production Data |  |  |  |  |  | 
Shift Length | 8 | Hours = | 480 | Minutes |  | 
Short Breaks | 2 | Breaks @ | 15 | Minutes Each = | 30 | Minutes Total
Meal Break | 1 | Breaks @ | 30 | Minutes Each = | 30 | Minutes Total
Downtime | 47 | Minutes |  |  |  | 
Ideal Run Rate | 60 | PPM (Pieces Per Minute) |  |  |  | 
Total Pieces | 19,271 | Pieces |  |  |  | 
Reject Pieces | 423 | Pieces |  |  |  | 
Support Variable | Calculation |  |  |  | Result | 
Planned Production Time | Shift Length - Breaks |  |  |  | 420 | Minutes
Operating Time | Planned Production Time - Downtime |  |  |  | 373 | Minutes
Good Pieces | Total Pieces - Reject Pieces |  |  |  | 18,848 | Pieces
OEE Factor | Calculation |  |  |  | My OEE% | 
Availability | Operating Time / Planned Production Time |  |  |  | 88.81% | 
Performance | (Total Pieces / Operation Time) / Ideal Run Rate |  |  |  | 86.11% | 
Quality | Good Pieces / Total Pieces |  |  |  | 97.80% | 
Overall OEE | Availability x Performance x Quality |  |  |  | 74.79% | 
OEE Factor | World Class | My OEE% |  |  |  | 
Availability | 90.00% | 88.81% |  |  |  | 
Performance | 95.00% | 86.11% |  |  |  | 
Quality | 99.90% | 97.80% |  |  |  | 
Overall OEE | 85.00% | 74.79% |  |  |  | 

## Slide 21: The Goal TPM
Regain confidence in our equipment:
Capability (make quality parts)
Effectiveness (eliminate delays)
Provide the operators with a machine environment that
enables them to produce good parts more easily

## Slide 22: TPM: Sharing responsibilities
Production
Top up fluids
Perform general maintenance
Clean interior/outside
Monitor machine condition
Call maintenance: detected or suspected problems
Maintenance
Perform specialised maintenance
Troubleshoot/fix actual and potential problems
Eliminate their root causes
Manufacturing Engineering
Improve maintainability and safety

## Slide 23: How Does TPM Differ From Regular Maintenance?
It is a proactive, team approach for maintenance
It is the responsibility of everyone, not just the maintenance department
Ensures safety and effective operation of equipment
Planned repairs rather than planned failure
Prevents equipment from breaking down
Prevents deterioration and prolongs the life cycle of the equipment

## Slide 24: TPM Principles
Increase Overall Equipment Effectiveness (OEE)
Upgrade operations and maintenance skills
Employee involvement through small group activities
A fact-based approach to continuous improvement

## Slide 25: TPM Provides Basic Stability for Lean Transformation
Focus of TPM
Stability
Heijunka Standardized Work Kaizen
Just-In-Time
Continuous flow
Takt time
Pull system
Flexible workforce
Jidoka
Separate man &
machine work
Abnormality Identification
Poka yoke
Visual Control
Goals:
highest quality,
lowest cost, shortest lead times
Involvement

## Slide 26: TPM is a Paradigm Shift
Old Attitude
TPM Attitude
I use
I maintain &
I fix
We maintain
Maintenance
Operator
Maintenance
Operator

## Slide 27: TPM Facilitates a Culture Change
Work Systems
& Processes
Behavior
Culture
The way we act
The way we think
Waste elimination
Attitude

## Slide 28: TPM Approach
Preventing breakdowns
Modifying equipment to prevent breakdowns and make maintenance easier
Designing and installing equipment that needs little maintenance
Making repairs as needed

## Slide 29: Eight Pillars (Strategies) of TPM
Office TPM
Safety, Health & Environment
Autonomous Maintenance
Planned Maintenance
Focused Improvement
Early Equipment
Management
Quality Maintenance
Education & Training
5S & Visual Management
TPM Goals:
Zero Defects, Zero Breakdowns,
Zero Accidents

## Slide 30: TPM Pillars & Activities 1
Pillar | Activities
Autonomous maintenance | Operator involvement in regular cleaning, inspection, lubrication, and learning about equipment to maintain basic conditions and spot signs of trouble
Planned maintenance | A combination of preventive, predictive, and proactive maintenance to avoid losses, and planned responses to fix breakdowns quickly
Focused equipment and process improvement | Measure of equipment- or process-related losses and specific improvement activities to reduce the losses
Education and training | A planned program for developing employee skills and knowledge to support TPM implementation

## Slide 31: TPM Pillars & Activities 2
Pillar | Activities
Quality maintenance | Activities to manage product quality by maintaining optimal operating conditions
Early equipment management | Methods to shorten the lead time for getting new equipment online and making defect-free products
Safety, health and environmental management | Safety and environmental training; integration of safety checks, visual controls, and mistake-proofing devices in daily work
Office TPM | TPM implementation in the supporting functions such as HR, Finance, Purchasing, etc.

## Slide 32: Total Quality Management

## Slide 33: Introduction to TQM Concepts
Total- As per the name suggests, it refers to the entire or whole organization.
Quality- Even this is self-explanatory, the quality of the company’s products and services.
Management- It can refer to the people running the organization and the way they manage, direct and control the organization.

## Slide 34: TQM
TQM refers to running the organization in an effective and productive manner and developing existing systems and procedures to operate at the highest efficiency. It also focuses on enhancing customer satisfaction and try to meet customer expectations.

## Slide 35: Total Quality Management Defined
TQM is based upon the principle that everyone in an organization must be responsible for quality.
The objective is that employees should seek to improve quality:
  by measurement
  ensuring quality at source
  through participative programmes
Key themes are:
  Involving everyone in the company (teamwork)
  continuous improvement
  right first time
  customer focus & satisfaction

## Slide 36: TQM Philosophy
The Approach .. Management led
The Scope……. Company-wide
The Scale ……. Everyone is responsible
The Philosophy … Prevention not detection
The Standard ….. Right-first-time
The Control…... Cost of quality
The Theme …... Continuous improvement

## Slide 37: Three Axioms of TQM (The Joiner Triangle)
Obsession with Quality
Commitment
Scientific Approach
Involvement
Logical Analytical
Approach
All one Team

## Slide 38: The Organizational Features of TQM
A focus on customer requirements.
A focus on product/service provision.
A commitment to improving quality and service at all levels
  development of an ethos.
A desire not only to ensure high quality, but also consistency.
Problem solving and decisions based upon teamwork approaches.
The adoption of a scientific approach to quality control and problem solving.
Development of long term partnerships with suppliers to ensure incoming quality.
Quest for perfection in product quality and delivery.

## Slide 39: Quality Certification & Accreditation
A means of "quality audit" for the quality assurance system.
A number of "standards" now exist where organizations can be certified by an institution or customer that they conform to a predetermined set of quality criteria.
Schemes include:
  ISO9000
  Ford Q1/Q101 schemes
  HEXCO in universities; ZIMSEC in schools

## Slide 40: ISO 9000
Based on BS5750, originally developed and administered by the British Standards Institute (BSI).
BS 5750 laid the foundation for the international standard office (ISO) equivalent, ISO 9000.
Now some companies and government departments' policy only to deal with companies possessing ISO9000 accreditation.
Caution: ISO9000 is a certification of quality assurance procedures, not a guarantee of product quality!

## Slide 41: Advantages of ISO 9000
According to The Providence Business News,
implementing ISO has the following
advantages:
Create a more efficient & effective operation
Increases customer satisfaction & retention
Reduces audits
Enhances marketing
Improves employee motivation, quality awareness & morale
Promotes international trade

## Slide 42: FUNCTIONS OF THE STANDARDS ASSOCIATION OF ZIMBABWE
Prepares and publishes Zimbabwe Standards,
Promotes an understanding of standards requirements by offering standards-based training programmes,
Provides technical services for the testing of raw material and manufactured goods
Promotes the widespread use of standards by operating various certification schemes, (e.g. ISO 9001, ISO 14001, OHSAS,18001, Hazard Analysis Critical Control Point and Product Mark Certification schemes)
Provides information services on national, foreign national, regional and international standards and technical regulations
Provides a World Trade Organization Technical Barriers To Trade enquiry point for standards and conformity assessment procedures information

## Slide 43: Criticisms of Quality Standards and Accreditation Schemes
Only an indication, not a guarantee of product or service quality.
Many organizations forced or feel obliged to register and receive such awards by their own customers.
The procedures and, in particular, documentation demanded by BS5750/ISO9000 is widely criticised as being overly bureaucratic.
Does physical existence of documentation and manuals necessarily mean that these procedures are followed?
Does the outside external auditor readily understand the operations in the organizations he/she visits?
The "gong mentality" - the pursuit of prizes for PR.

## Slide 44: TQM: Critical Issue 1
What comprises TQM varies considerably between different organizations - different programmes and emphases.
  So, it is often difficult to link causes with effects when assessing the success of TQM programmes in some organizations.

## Slide 45: TQM: Critical Issue 2
The ease with which some companies have claimed to have changed their organization cultures can be questioned:
  Culture runs deeper than attitudes: it relates to the underlying assumptions, beliefs and values of people.
  Culture is, in any case, used rather too loosely by supporters of TQM: do they always understand exactly what is meant by the term corporate culture?

## Slide 46: TQM: Critical Issue 3
Co-ordinators of TQM programmes can often appear very patronising to others in the organization:
for example, they often state that the "operators are the real experts in their work and so should be the ones to suggest improvements".
might be the case, but is self-evident to the operators themselves - they may have had years of frustration not having had their voices heard!

## Slide 47: TQM: Critical Issue 4
TQM an umbrella term - its implementation involves the introduction of the various quality improvement - criticisms of these:
  quality initiatives are frequently introduced with a veneer of developing customer focus/ increased industrial democracy, but often the motivation is to increase their relative power over workers and trade unions.
  Hence, quality in itself is difficult to argue against, but much (probably valid) scepticism.