## Slide 1: Value Stream Mapping & Control Charts

## Slide 2: Value Stream Mapping Definition
Value Stream Mapping (VSM): – Special type of flow chart that uses symbols known as "the language of Lean" to depict and improve the flow of inventory and information.

## Slide 3: Value Stream Purpose
Once someone maps the current state of the process from beginning to end, he or she should find areas that do not add value to the process and reduce those areas.

## Slide 4: Why?
Many organizations pursuing “lean” conversions have realized that improvement events alone are not enough
Improvement events create localized improvements, value stream mapping & analysis strengthens the gains by providing vision and plans that connect all improvement activities
• Value stream mapping & analysis is a tool that allows you to see waste, and plan to eliminate it

## Slide 5: What is Value?
capability provided to a customer
– of the highest quality,
– at the right time,
– at an appropriate price,
as defined by the customer.
• "Value" is what the customer is buying

## Slide 6: What Is Value Stream Analysis?
Planning tool to optimize results of eliminating waste

## Slide 8: Value Added Non Value Added
Examples: moulding welding, adding components | Value Added Adds real value or worth to the product. Usually something the customer pays for.
Examples: handling, adjusting, bending, walking, reworking, reaching, inspecting, searching, reading, packing, waiting | Non- Value Added Does not add real value or quality to the product. Assumes activities have to occur in order to do the job.

## Slide 9: VSM Icons

## Slide 10: Where do we start?
A3 Paper, Pencil and inquiring set of minds….
Define the process to be mapped and bound the process (Supplier – Customer)
Create a process box for each process step.

## Slide 11: Map the Process flow

## Slide 12: Information flows
Adding information flow is one thing that differentiates VSM from other techniques.
It helps identifies placing of orders and scheduling of work is done.

## Slide 13: Add Information flow

## Slide 14: Collect Process Data
Next we need to record the process data for our process, this data can include the following:
Inventory
Scrap rate
Pallet size
Uptime
Changeover time
Cycle time
Net available working time
Number of operators

## Slide 15: Data box in VSM
A data box is a box drawn on a value stream map to illustrate and show data that is related to the process on the value stream map. Some types of data that are commonly held within a data box are:
Cycle Time
Process Time
Yield
Lead Time
Changeover Time
Number of Shifts

## Slide 16: Add The Data

## Slide 17: Creating a timeline
It shows how long inventory remains in the system
How long a product is processed for
Processing time to process one item
Use inventory and daily demand to calculate how many days of inventory you have.

## Slide 18: Analyse the data

## Slide 19: What does our VSM tell us
The timeline tells us that product takes only 8 minutes to be processes but a single piece of inventory can be within the organisation for over 8 days..
The data boxes show us which processes have long changeovers or poor quality performance and other issues

## Slide 20
Moving from Current State to Ideal State

## Slide 21: Control Chart
These charts are used to check, whether process data remains under control for the shorter time span.
They involve process control limits and sometimes customer specification limits as operational ranges or bands.
Process data is analyzed to remain within process control limits. Whenever data goes out of control limits, it certainly has some special causes – to be investigated & removed immediately.
The aim of these charts is to ensure process data doesn’t go beyond control limits.
However, some exception rules are also there to ascertain the condition of a process going out of control, while well within control limits.

## Slide 22: CONTROL CHARTS
A graph that establishes control limits of a process
Control limits
  upper and lower bands of a control chart
Types of charts
  Attributes
    p-chart - uses portion defective in a sample
    c-chart -uses number of defects in an item
  Variables
    range (R-chart)
    mean (x bar – chart)
Attribute charts require larger sample sizes of 50 to 100 parts
Variable charts require smaller samples of 2 to 10 parts in a sample

## Slide 23: PROCESS CONTROL CHART
1
2
3
4
5
6
7
8
9
10
Sample number
Upper
control
limit
Process
average
Lower
control
limit
Out of control

## Slide 24: A PROCESS IS IN CONTROL IF …
… no sample points outside limits
… most points near process average
… about equal number of points above and below centerline
… points appear randomly distributed